## Slide 1: Chapter 6
Interrupt and Exception Programming

## Slide 2: Polling vs. Interrupts

## Slide 3: NVIC in ARM Cortex-M

## Slide 4: Interrupt Vector Table for ARM Cortex-M
Interrupt # | Interrupt | Memory Location (Hex)
 | Stack Pointer initial value | 0x00000000
1 | Reset | 0x00000004
2 | NMI | 0x00000008
3 | Hard Fault | 0x0000000C
4 | Memory Management Fault | 0x00000010
5 | Bus Fault | 0x00000014
6 | Usage Fault (undefined instructions, divide by zero, unaligned memory access,...) | 0x00000018
7 | Reserved | 0x0000001C
8 | Reserved | 0x00000020
9 | Reserved | 0x00000024
10 | Reserved | 0x00000028
11 | SVCall | 0x0000002C
12 | Debug Monitor | 0x00000030
13 | Reserved | 0x00000034
14 | PendSV | 0x00000038
15 | SysTick | 0x0000003C
16 | IRQ 0 for peripherals | 0x00000040
17 | IRQ 1 for peripherals | 0x00000044
… | … | …
255 | IRQ 239 for peripherals | 0x000003FC

## Slide 5: Going from Reset to Boot Program

## Slide 6: ARM Cortex-M Stack Frame upon Interrupt

## Slide 7: Main Program gets interrupted

## Slide 8: Interrupt Priority for ARM Cortex-M
Interrupt # | Interrupt | Priority Level
0 | Stack Pointer initial value | 
1 | Reset | -3 Highest
2 | NMI | -2
3 | Hard Fault | -1
4 | Memory Management Fault | Programmable
5 | Bus Fault | Programmable
6 | Usage Fault (undefined instructions, divide by zero, unaligned memory access,....) | Programmable
7 | Reserved | Programmable
8 | Reserved | Programmable
9 | Reserved | Programmable
10 | Reserved | Programmable
11 | SVCall | Programmable
12 | Debug Monitor | Programmable
13 | Reserved | Programmable
14 | PendSV | Programmable
15 | SysTick | Programmable
16 | IRQ 0 for peripherals | Programmable
17 | IRQ 1 for peripherals | Programmable
… | … | Programmable
255 | IRQ 239 for peripherals | Programmable

## Slide 9: CONTROL Register in ARM Cortex-M4
nPRIV (Privilege): Defines the Thread mode privilege level 0: Privileged 1: Unprivileged Active Stack Pointer (ASP): Defines the currently active stack pointer (ASP = SPSEL) 0: MSP is the current stack pointer. 1: PSP is the current stack pointer. Floating Point Context Active (FPCA) 0: No floating point context active. 1: Floating point context active.

## Slide 10: Privileged level Execution and Processor Modes in ARM Cortex-M
Processor Mode | Software | Privilege level
Thread | Applications | Privileged and Unprivileged
Handler | ISR for Exceptions and IRQs | Always Privileged
In Thread mode, use bit 0 of the CONTROL register to select Privileged or Unprivileged |  | 

## Slide 11: Processor Modes and Stack Usage in ARM Cortex-M
Processor Mode | Software | Stack Usage
Thread | Applications | MSP or PSP
Handler | ISR for Exceptions and IRQs | MSP
Note: In Thread mode, use bit 1 of the Control register to select MSP or PSP for stack pointer. |  | 

## Slide 12: Processor Mode, Privilege, and Stack in ARM Cortex
Mode | Privilege | Stack Pointer | Typical Example usage
Handler | Privileged | Main | Exception Handling
Handler | Unprivileged | Any | Reserved since Handler is always Privileged
Thread | Privileged | Main | Operating system kernel
Thread | Privileged | Process | 
Thread | Unprivileged | Main | 
Thread | Unprivileged | Process | Application threads

## Slide 13: ARM Cortex-M Registers

## Slide 14: Special function registers of ARM Cortex-M
Register name | Privilege Usage
MSP (main stack pointer) | Privileged
PSP (processor stack pointer) | Privileged or Unprivileged
PSR (Processor status register) | Privileged
APSR (application processor status register) | Privileged or Unprivileged
ISPR (interrupt processor status register) | Privileged
EPSR (execution processor status register) | Privileged
PRIMASK (Priority Mask register) | Privileged
FAULTMASK(fault mask register) | Privileged
BASEPRI (base priority register) | Privileged
CONTROL (control register) | Privileged
Note: We must use MSR and MRS instructions to access the above registers | 

## Slide 15: IRQ assignment in Tiva ARM TM123GH6PM
INT# | IRQ# | Vector location | Device
1-15 | none | 0000 0000 to 0000 003C | CPU Exception (set by ARM)
16 | 0 | 0000 0040 | GPIO PORT A
17 | 1 | 0000 0044 | GPIO PORT B
18 | 2 | 0000 0048 | GPIO PORT C
19 | 3 | 0000 004C | GPIO PORT D
20 | 4 | 0000 0050 | GPIO PORT E
21 | 5 | 0000 0054 | UART0
22 | 6 | 0000 0058 | UART1
23 | 7 | 0000 005C | SSI0
24 | 8 | 0000 0060 | I2C0
25 | 9 | 0000 0064 | PWM0 Fault
26 | 10 | 0000 0068 | PWM0 Generator 0
27 | 11 | 0000 006C | PWM0 Generator 1
28 | 12 | 0000 0070 | PWM0 Generator 2

## Slide 16: IRQ assignment in Tiva ARM TM123GH6PM(Cont.)
INT# | IRQ# | Vector location | Device
29 | 13 | 0000 0074 | QEI0
30 | 14 | 0000 0078 | ADC0 Sequence 0
31 | 15 | 0000 007C | ADC0 Sequence 1
32 | 16 | 0000 0080 | ADC0 Sequence 2
33 | 17 | 0000 0084 | ADC0 Sequence 3
34 | 18 | 0000 0088 | Watchdog Timers 0 and 1
35 | 19 | 0000 008C | 16/32-Bit Timer 0A
36 | 20 | 0000 0090 | 16/32-Bit Timer 0B
37 | 21 | 0000 0094 | 16/32-Bit Timer 1A
38 | 22 | 0000 0098 | 16/32-Bit Timer 1B
39 | 23 | 0000 009C | 16/32-Bit Timer 2A
40 | 24 | 0000 00A0 | 16/32-Bit Timer 2B
41 | 25 | 0000 00A4 | Analog Comparator 0
42 | 26 | 0000 00A8 | Analog Comparator 1

## Slide 17: IRQ assignment in Tiva ARM TM123GH6PM(Cont.)
INT# | IRQ# | Vector location | Device
43 | 27 | - | Reserved
44 | 28 | 0000 00B0 | System Control
45 | 29 | 0000 00B4 | Flash Memory Control and EEPROM Control
46 | 30 | 0000 00B8 | GPIO Port F
47-48 | 31-32 | - | Reserved
49 | 33 | 0000 00C4 | UART2
50 | 34 | 0000 00C8 | SSI1
51 | 35 | 0000 00CC | 16/32-Bit Timer 3A
52 | 36 | 0000 00D0 | 16-32-Bit Timer 3B
53 | 37 | 0000 00D4 | I2C1
54 | 38 | 0000 00D8 | QEI1
55 | 39 | 0000 00DC | CAN0
56 | 40 | 0000 00E0 | CAN1
57-58 | 41-42 | - | Reserved

## Slide 18: IRQ assignment in Tiva ARM TM123GH6PM(Cont.)
INT# | IRQ# | Vector location | Device
59 | 43 | 0000 00EC | Hibernation Module
60 | 44 | 0000 00F0 | USB
61 | 45 | 0000 00F4 | PWM Generator 3
62 | 46 | 0000 00F8 | µDMA Software
63 | 47 | 0000 00FC | µDMA Error
64 | 48 | 0000 0100 | ADC1 Sequence 0
65 | 49 | 0000 0104 | ADC1 Sequence 1
66 | 50 | 0000 0108 | ADC1 Sequence 2
67 | 51 | 0000 010C | ADC1 Sequence 3
68-72 | 52-56 | - | Reserved
73 | 57 | 0000 0124 | SSI2
74 | 58 | 0000 0128 | SSI3
75 | 59 | 0000 012C | UART3
76 | 60 | 0000 0130 | UART4

## Slide 19: IRQ assignment in Tiva ARM TM123GH6PM(Cont.)
INT# | IRQ# | Vector location | Device
77 | 61 | 0000 0134 | UART5
78 | 62 | 0000 0138 | UART6
79 | 63 | 0000 013C | UART7
80-83 | 64-67 | - | Reserved
84 | 68 | 0000 0150 | I2C2
85 | 69 | 0000 0154 | I2C3
86 | 70 | 0000 0158 | 16/32-Bit Timer 4A
87 | 71 | 0000 015C | 16/32-Bit Timer 4B
88-107 | 72-91 | - | Reserved
108 | 92 | 0000 01B0 | 16/32-Bit Timer 5A
109 | 93 | 0000 01B4 | 16/32-Bit Timer 5B
110 | 94 | 0000 01B8 | 32/64-Bit Timer 0A
111 | 95 | 0000 01BC | 32/64-Bit Timer 0B
112 | 96 | 0000 01C0 | 32/64-Bit Timer 1A

## Slide 20: IRQ assignment in Tiva ARM TM123GH6PM(Cont.)
INT# | IRQ# | Vector location | Device
113 | 97 | 0000 01C4 | 32/64-Bit Timer 1B
114 | 98 | 0000 01C8 | 32/64-Bit Timer 2A
115 | 99 | 0000 01CC | 32/64-Bit Timer 2B
116 | 100 | 0000 01D0 | 32/64-Bit Timer 3A
117 | 101 | 0000 01D4 | 32/64-Bit Timer 3B
118 | 102 | 0000 01D8 | 32/64-Bit Timer 4A
119 | 103 | 0000 01DC | 32/64-Bit Timer 4B
120 | 104 | 0000 01E0 | 32/64-Bit Timer 5A
121 | 105 | 0000 01E4 | 32/64-Bit Timer 5B
122 | 106 | 0000 01E8 | System Exception (imprecise)
123-149 | 107-133 | - | Reserved
150 | 134 | 0000 0258 | PWM Generator 0
151 | 135 | 0000 025C | PWM Generator 1
152 | 136 | 0000 0260 | PWM Generator 2
153 | 137 | 0000 0264 | PWM Generator 3
154 | 138 | 0000 0268 | PWM1 Fault

## Slide 21: Interrupt enabling with all 3 levels

## Slide 22: GPIO Interrupt Mask (GPIOIM)

## Slide 23: Interrupts 0–31 Set Enable (EN0)

## Slide 24: Interrupts 32–63 Set Enable (EN1)

## Slide 25: Interrupts 64–95 Set Enable (EN2)

## Slide 26: Interrupts 94–127 Set Enable (EN3)

## Slide 27: Interrupts 0–31 Clear Enable (DIS0)

## Slide 28: Interrupts 32–63 Clear Enable (DIS1)

## Slide 29: Interrupts 64–95 Clear Enable (DIS2)

## Slide 30: Interrupts 96–127 Clear Enable (DIS3)

## Slide 31: Enabling and Disabling an Interrupt

## Slide 32: GPIO Interrupt Sense (GPIOIS)

## Slide 33: GPIOIEV

## Slide 34: UART Interrupt Registers

## Slide 35: Using GPIOIM and GPIOIEV Registers
IS.n (interrupt sense) | IEV.n (Interrupt Event) | 
0 | 0 | Falling edge
0 | 1 | Rising edge
1 | 0 | Low level
1 | 1 | High level

## Slide 36: UART Interrupt Mask (UARTIM)

## Slide 37: GPTM Interrupt Mask (GPTMIMR)

## Slide 38: SysTick Internal Structure

## Slide 39: SysTick Control and Status Register (STCTRL)

## Slide 40: SysTick Counting

## Slide 41: PRIn Registers